## Slide 1
Scenarios 2024 Modelling Methodologies

## Slide 2: TYNDP 2024 Scenarios Strategy
National Trends+ scenario
Deviation scenarios
2022
2030
2040
2050
Increasing range of uncertainty
2035
snapshots
The aggregation of national approaches that reaches EU targets
Deviation from National Trends + scenario to capture uncertainties and reach EU targets
Fit-for-55 or REPowerEU

## Slide 3: Overview of 2024 Innovations
The innovations implemented in the TYNDP 2024 Scenarios seek to improve those already implemented in TYNDP 2022(1).
The aim is to enhance the representation of a fast-changing energy system and the integration of its different sectors.
The following slides will describe the new methodologies used in the current cycle.
(1) TYNDP 2022 Scenario Building Guidelines: https://2022.entsos-tyndp-scenarios.eu/building-guidelines/

## Slide 4: Overview of 2024 Innovations
Tool Chain for TYNDP 2024 Scenarios:
ETM replacing Ambition Tool
DFT replacing TRAPUNTA

## Slide 5: Overview of 2024 Innovations
1
Hydrogen Modelling
Hydrogen zones will be modelled considering a hydrogen market and production outside the market.
Domestic production of synthetic fuels.
Explicit hydrogen to power modelling.
2
EV Modelling
Improvement of 2022 scenarios.
Transport modelling will include demand side shifting and Vehicle to grid.
Offshore Modelling (*)
Modelling of offshore wind hubs.
Hubs include wind farms, electricity grid, hydrogen pipelines and electrolysers.
Hubs will interconnect with each other and mainland Europe.
3
4
Heat Modelling
The 2024 Scenario Building process explicitly considers hybrid heat pumps as heating technology (boiler and electric heat pump) that use energy produced by three carriers (electricity, hydrogen and methane).
5
Expansion Modelling
New approach that enhances run times over previous cycle, and allows for a larger model to be run
(*) Only innovation implemented in NT+ Scenario with no expansion. See slide 7.

## Slide 6: Scenario 2024 Modelling topology
Residential & Tertiary
Demand
PV
Battery
Electricity Market
Generation Capacity
Infrastructure
Demand
EV Electric Vehicle
Battery
Demand
SRES
P2G
YY00
Demand
Storage
DRES
P2G
H2 Imports
SNG
Demand
e-Kerosene
Demand
E-Diesel
Demand
P2G
Zone 1
Demand
Tank Storage
SMR
Offshore Hub
Hybrid Heating
P2G
Biogenic CO2
Zone 2
XXe
XXh2
XXh2 Hub
XXe Hube

## Slide 7: TYNDP 2024 NT+ Scenario Topology
H2 Node
Electricity Node
Offshore Wind Hub
NT+ Scenario uses a simplified methodology compared to Deviation Scenarios because it does not require an expansion and uses directly predefined demand and capacity figures resulting from TSO data collection.

## Slide 8: Hydrogen Modelling

## Slide 9: Hydrogen Configurations
TYNDP 2022 Scenarios considered 4 different configurations for P2G and H2 grid. However, TYNDP 2024 Scenarios aggregate them into 2 zones:
Zone 1 includes:
  Direct H2 demand
  Steel Tank H2 Storages
  Steam Methane Reformers
  Shared RES
Zone 2 follows the same approach as Configuration 4 in 2022 Scenarios:
  Salt Cavern Storages
  H2 grid
  Imports (H2 and ammonia)
  Dedicated RES
Synthetic Fuels are also explicitly modelled as a new development.

## Slide 10: Synthetic Fuels
FR00
H2-Z2
Traditional Supply/Imports
Demand
FR00
Power
€
DE00
H2-Z2
DE00
Power
η, €
η, €
Synthetic fuels are modelled as 1 commodity market within Europe (one single node per fuel type)
This node will contain a demand and any country can feed into this node
This assumes there are no bottlenecks in the oils and methane pipeline network
Fuels will first be created using biogenic CO2. once this has been exhausted import will be used.
CO2 Supply

## Slide 11: Synthetic Fuel costs
Synthetic Fuels
Synthetic fuels will be produced using CO2 first, then imports will be used.
CO2 will be modelled as zero cost as it is incredibly difficult to find a commodity cost for this gas.
The import cost will be set a 1EUR above the ammonia import price to ensure this fuels are produced nationally first.

## Slide 12: Hydrogen Demand
ETM quantifies the use of energy across different energy carriers, sectors and applications.
Annual hydrogen demand’s split follows ETM outputs per country. In order to obtain 1 hourly H2 demand profile per country, the following data is used:
Heating
Prosumer: Hydrogen Boilers  using heating normalized profiles from DFT (open power system)
Industrial: High Temperature Heating  flat profile
Transport
Aviation: Historical kerosene profiles – (Eurostat)
Heavy Duty Vehicles: Flat Profile
Industry
Final Hydrogen Demand: Flat profile
Synthetic fuel production  historical profiles from the industry using the fuel – (Eurostat or Flat)

## Slide 13: Demand Split
H2 node | Sector | 2025 | 2030 | 2040 | 2050
Zone 1 | Feedstock | 75 | 60 | 30 | 10
 | Industry – Energetic | 50 | 50 | 30 | 15
 | Transport | 75 | 50 | 25 | 15
Zone 2 | Feedstock | 25 | 40 | 70 | 90
 | Industry – Energetic | 50 | 50 | 70 | 85
 | Prosumer Heat | 100 | 100 | 100 | 100
 | Transport | 25 | 50 | 75 | 85
The hydrogen demand must be split into the 2 Zones.
They will be split by the 4 sectors
Feedstock
Process heat
Prosumer heat
Transport
The synthetic fuel production will be assigned to zone 2.
They may be connected to refineries which can be classed as feedstock. Therefore, the connections to synthetic fuel will mirror the split for feedstock

## Slide 14: Hydrogen Steel Tanks – Zone 1
Used in the industrial sector as a buffer to smoothen the intermittency of RES
Steel tanks capacity is calculated as follows:
Share of industrial customers in Zone 1 (50% - 15%)
25% of those customer will have steel tanks
Steel tanks will be able to cover 1 days demand
E.g.
In 2040, 7.5% of industrial demand will have steel tanks associated
In 2050, 3.25% of industrial demand will have steel tanks associate

## Slide 15: Synthetic Fuel Demand
E-fuels
E-Kerosene  historical Kerosene profiles
E-Diesel  Flat profiles
Synthetic Methane
Synthetic fuel production  historical Methane profiles

## Slide 16: Explicit hydrogen to power modelling
Some countries are expected to have hydrogen-fuelled thermal power plants in the long term.
Electricity/gas TSOs have provided H2 CCGT capacities for target years within the TYNDP data collection.
TYNDP 2024 Scenarios introduce the explicit hydrogen to power modelling, allowing the H2 needed to power CCGTs to come from the H2 market rather than from a supposedly infinite fuel source (as with other fuels for which no market has been modelled, e.g. coal):
H2 CCGTs in the Electricity Market node are linked to the Hydrogen Market nodes in Plexos.
H2 demand will increase proportionally to the fuel offtake of these power plants.
H2 Zone 2
Electricity Node
H2 Demand = H2 Demand (input) + CCGT Fuel Offtake
CCGT Fuel Offtake
Electricity Generation

## Slide 17: EV Modelling

## Slide 18: EV Modelling
TYNDP 2022 Scenarios topology considered an EV Node which was connected to both the Prosumer and the Electricity Market Nodes. Vehicles were modelled as batteries, being able to charge from the grid to meet the node’s demand (MWh instead of km) and to feed electricity into the grid (V2G).
TYNDP 2024 Scenarios consider an 'EV Street' Node connected to the e-market Node, and an 'EV Home' Node connected to the Prosumer Node. Vehicles are also modelled as batteries, and they are able to charge from the grid and to provide V2G.
Vehicles will charge at home or in the street depending on the input availability profiles of these stations, and the timing of charging will be optimized based on costs.
They will also be able to feed electricity into the grid (V2G).
Fast charging is not price driven, so it is not modelled, and its electricity profiles are included in the final electricity demand.

## Slide 19: Electric Vehicle topology
Electricity Node
Prosumer Node
EV Street Node
Charge/Discharge η = 94%
Demand (MWh) = Total km * 170 Wh/km * %EVs
EV Battery Capacity = Nº EVs * Unitary Capacity * %EVs
EV Battery Power = Nº EVs * Unitary Charge Rate * Availability Profile * %EVs
Min SoC
Demand (MWh) = Total km * 170 Wh/km * %EVs
Capacity = Charging Station Charge Rate * Nº EVs * Availability Profile * %EVs
Wheeling Charge = UoS Cost
EV Home Node
Capacity = Charging Station Charge Rate * Nº EVs * Availability Profile * %EVs * %V2G
Wheeling Charge = UoS Cost
Idem
Idem

## Slide 20: Electric Vehicle & Charging Station Properties
Parameter | Value |  |  |  |  | 
Number of EVs | ETM values per country and Target Year |  |  |  |  | 
Capacity (kWh/Vehicle) |  | 2030 | 2035 | 2040 | 2045 | 2050
 | DE | 60 | 72 | 83 | 92 | 100
 | GA | 54 | 66 | 72 | 81 | 90
Efficiency (Wh/km) | 170 |  |  |  |  | 
Demand (km/Vehicle) | ETM values per country and Target Year converted into hourly profiles based on REM2030 (i) |  |  |  |  | 
Max Charge/Discharge Rate (kW/Vehicle) | 7.4 |  |  |  |  | 
Initial SoC (%) | 50 |  |  |  |  | 
Min SoC (%) | profile |  |  |  |  | 
Home Charger Share (%) | Availability profiles (ii) based on platform used by ETM (iii) |  |  |  |  | 
Street Charger Share (%) | Availability profiles (ii) based on platform used by ETM (iii) |  |  |  |  | 
(i ) https://rem2030.de/rem2030-de/REM-2030-Driving-Profiles.php
(ii) The availability profile outline the share of vehicles which can be charged by a particular type of charging station.
The share will be split between weekdays/weekends and by station type (Home, Street, Fast)
(iii) https://platform.elaad.io/analyse/charging/
Electric Vehicle
Parameter | Home | Street
Max Charge/Discharge Rate (kW/Vehicle) | 7.4 | 16
Use of System Charge (€/MWh) | 30 | 35
Charge/Discharge Efficiency (%) | 94 | 94
Charging Stations
It is important that the values used for modelling EVs in the TYNDP 2024 Scenarios represent the average European EV owner in the best way.
In 2022 approximately 1.5 million EVs were sold in Europe across multiple models (1). Most EV models are available in standard and long range, with different sized battery capacities. Using publicly available data on useable battery capacities of EV models, a weighted average is calculated for 2030, based on the EVs sold in Europe in 2022 (2).
To be in line with the storylines of TYNDP 2024, it is determined that Distributed Energy will apply the higher ranges of battery capacities of EVs sold in 2022, while Global Ambition will apply the lower ranges.
It is assumed that technological developments in battery capacities and EV design will drive an increase in EV battery capacities towards 2050.
Additionally, it is assumed that charging stations at home and by the streets is an average of what is currently on the market. The methodology on these charging stations is limited to 22 kW. Higher capacity charging stations are handled separately in the modelling.
(1) https://www.jato.com/volkswagen-led-the-european-electric-vehicle-market-in-2022/
(2) Compare electric vehicles - EV Database (ev-database.org)

## Slide 21: Electric Vehicle & Charging Station Properties
AVAILABILITY PROFILE = % of EVs that can be charging at home or in the street
%EVs = % of EVs that have access to a charging point (on top of the av.profile)
%V2G = % of EVs that can provide V2G (on top of av.profile and %EVs)
 | 2030 | 2040 | 2050
Street | 30% | 30% | 30%
Home | 70% | 70% | 70%
 | 2030 | 2040 | 2050
DE | 30% | 40% | 50%
GA | 15% | 20% | 25%
%V2G Prosumer
%EVs
 | 2030 | 2040 | 2050
DE | 0% | 10% | 20%
GA | 0% | 5% | 10%
%V2G Street

## Slide 22
Min SoC

## Slide 23: EV Prosumer – Energy Usage
Chart: 

## Slide 24: Offshore Modelling

## Slide 25: Co-optimized offshore energy and infrastructure build-out
simplicity
ACCURACY
  In the TYNDP22 Scenarios all offshore capacity build out was connected radially to their respective home market
  TYNDP24 Scenarios will jointly build out offshore capacity and infrastructure
  Capacity and infrastructure will be build out aggregated in so-called "offshore hubs" as a trade-off between simplicity and accuracy
  Offshore hubs represent aggregated PECD areas within the model

## Slide 26: Offshore Hubs - definition
  Offshore Hubs concept reflects the combined buildout of offshore energy and infrastructure to multiple demand areas
  In general, a distinction is made between the near-shore (<50 km) and the far-shore PECD zone (>50 km)
    Offshore Bidding Zone (OBZ) – Individual price area for each hub (aggregated PECD areas) to reduce model complexity
    Near shore zone - Radially connected offshore to HomeMarket
    Exclusion zone for the nearest 12 nm to account for shoreline protection and reflect the NIMBY effect of coastal communities

## Slide 27: Offshore Hubs - Assumptions
  Interconnector options will be restricted to connecting neighbouring Offshore Hubs (neighbouring aggregated PECD zones) and to related HomeMarket
  Hub infrastructure will be connected from mid-point to mid-point + a 30 % cable routing factor on top (as in the NSWPH methodology)
  The length of the infrastructure to shore will be distance to shoreline + 30 km
  Hubs and their related home markets can be connected via DC cables as well as H2 pipelines
  Wind offshore capacity within the hubs can be build either connected to the electricity or H2 grid (via integrated offshore electrolysers). Additionally, platform-based electrolysers to link the electricity and H2 grid can be build out.

## Slide 28: Full Topology

## Slide 29: Offshore technology costs: Bathymetry data
Methodology
Exclude area till 12 nautical miles (22.2 km) as customary minimal distance from shore: ref 1. (p. 5)
Distinguish between fixed-bottom and floating technologies
  Reasoning: cost difference
  Reference: Offshore cost elicitation survey (p. 560)
  Differentiating factor: water depth
    Fixed-bottom: 0-60m ref 2. (p. 7) & ref 3. (p. 6)
    Floating: 60m-1000m ref 4. (p. 558)
    Water depth limit of 1000m ref 2. (p. 7) & : ref 3. (p. 4)
  Final approach after exchange with WindEurope
    CostBand 1 (0-200m): Fixed-Bottom & Floating (shallow)
    CostBand 2 (200-1000m): Floating (deep)
AC to DC break-even point at 50km from shore ref 5. (p. 5)

## Slide 30: Wind Offshore – Investment Candidates
  Wind Offshore Fixed AC Radial
  Wind Offshore Floating AC Radial
  Wind Offshore Fixed DC Radial*
  Wind Offshore Floating DC Radial*
  Wind Offshore Fixed Hub
  Wind Offshore Floating Hub
  Wind Offshore Fixed Hub H2
  Wind Offshore Floating Hub H2
  Electrolyzer Offshore
  H2 Pipeline
  HVCD Cable
  Onshore HVDC Station
Components
  Electrolyzer Offshore
  H2 Pipeline
Includes turbine, foundation, installation, array cables, platform
Cable cost Mio.€/MW/km
Expansion possible
Compressor costs in pipeline included
Example E-Hub
* Radial DC connections are only used in special cases, e.g. in Italy
  Wind Offshore Fixed Hub
  HVCD Cable
Hub2Hub
connection
  HVCD Cable
  Onshore HVDC Station
Hub connection to HomeMarket

## Slide 31
AC Electricity Grid DC Electricity Grid Electricity and Gas Grid Hydrogen Pipeline
Exemplary types of offshore wind farms

## Slide 32: Hub Structure
Plattform A Radial i
Plattform B Radial i
Plattform C Radial i
Plattform C
Plattform B
E-Wind
Plattform A
Substation
Radial i
Plattform A Hub x
Plattform B Hub x
Plattform C Hub x
Substation
Hub
E-Node Dedicated
Hub
E-Node Grid
Hub
H2-Node
Hub x
Gas station
Inter-Hub H2 pipelines
Plattform C
Plattform B
H2-Wind
Plattform A
Plattform C
Plattform B
E-Wind
Plattform A
Grid P2G
Dedicated P2G
Hub z
Hub y
Onshore Zone i
Zone i E-Node
Onshore P2G
Zone i H2-Node
H2 Power Generation
Other Supply/Demand
Other Supply/Demand
Onshore Zone j
Inter-Hub DC connections

## Slide 33: Usage of Bathymetry data in order to differentiate Offshore technology costs
12nm (22 km)
50 km
HomeMarket (AC)
OBZ (Hubs) (DC)
Offshore
HomeMarket (AC)
FB
FL
12nm Zone (excluded)
OBZ (Hubs) (DC)
FB
E
H2
E
H2
FL
Hub
(excluded)
Fixed-Bottom
&
Floating (shallow)
(0-200m)
Floating (deep)
(200m-1000m)
xx km
HM
Carrier/ Infrastructure
Foundation type
Zone

## Slide 34: Heat Modelling

## Slide 35: Heat Demand
ETM provides annual Flexible Space & Water Heating demand, which is divided into 2 categories:
Prosumer Heating: To be supplied by Hybrid Heat Pumps (explicitly modelled in PLEXOS for the first time in TYNDP 2024 Scenarios). The electricity/gas that HHP require are a result of the optimization of the model.
District Heating: The electricity/gas that these Heat sources require is given by ETM and integrated into the final electricity and gas demand profiles (the same approach as TYNDP 2022 Scenarios)

## Slide 36: Hybrid Heat Pumps Demand
ETM tool provides Heat demand figures for Climate Year 2019.
A methodology has been developed to obtain hourly heat demand hourly profiles per country and for CY 1982-2019:
Based on Open Power System Data - When To Heat (1) demand profiles
Data available for all EU27 countries
Data available from 2008 to 2020
Data from 1982 – 2019 must be calculated
Regression analysis performed to understand the relationship between temperature and heat demand
Model in trained on years 2008 to 2013
Heat demand for all years can be calculated using the trained model
(1) Data Platform – Open Power System Data (open-power-system-data.org)

## Slide 37: Climate Data: Linear Regression Analysis
The straight line equation is used to calculate the heat demand:
Climate variability data:
The mean value per hour is calculated over all climates
The variance from the mean for each climate year is then calculated in %.

## Slide 38: Creation of demand timeseries
The demand timeseries is split into 2 parts. The first part is Space heating and the other is water heating.
The water heating profiles are not climate dependant and is multiplied by countries water heating profiles
The space heating profile is developed in the following steps
  The most representative climate year per country is used as the base heating profile.
  This heating profile is multiplied by the Annual heating demand
  The heating profiles is then multiplied by the climate variability data in order to give the climate profiles

## Slide 39: Hybrid Heat Pumps Modelling
Hybrid Heat Pumps (HHP) combine an electric heat pump with a gas (H2 or CH4) boiler. Each of them will work depending on the outside temperature (COP curves).
The number of HHP per country and their capacities are given by ETM. However, due to the way they are modelled in PLEXOS, HHP capacities in the model are equal to the peak heat demand in the node they are connected to.
H2 HHP:
  The electric heat pump is connected to the Prosumer Node
  The H2 boiler is connected to H2 Zone 2 Node
    Heat Rate = 0.93 GJ/GJ
CH4 HHP:
  The electric heat pump is connected to the Prosumer Node
  The CH4 boiler is fuelled with CH4 (non-modelled market)
    Heat Rate = 0.93 GJ/GJ

## Slide 40: Coefficient Of Performance
Climate and country dependant COP curves are calculated following ETM’s formula:
COPT = base COP + COP per degree * T
where
T is ambient temperature
base COP = 2.32333
COP per degree = 0.05783

## Slide 41: Expansion Modelling

## Slide 42: Expansion Model
For a defined electricity and H2 demand, different electricity and H2 systems can be thought of.
PLEXOS has investment loop capabilities from which Scenarios will benefit to define different infrastructure pathways towards a decarbonized energy system in 2050.
TYNDP 2022 Scenarios used a multi-temporal approach: 25 years were run (2025-2050).
The optimization problem was divided into 8 sub-time horizons of 5 years with a 2-year overlap. However, execution times were too high and the granularity of the simulation was too low, which meant that batteries could not expand (their behaviour was not visible using this granularity)
TYNDP 2024 introduce a new approach to the multi-temporal expansion. Execution times are significantly reduced and the granularity used allows the expansion of batteries.

## Slide 43: 2024 Expansion Approach
TYNDP 2024 Scenarios cover a 20-year horizon (2030-2050).
A new methodology has been developed to turn those 20 years into 5 and reduce the optimization problems complexity.
Target Years are 2030, 2035, 2040, 2045, 2050, and these are the only years modelled in PLEXOS. However, inputs must ensure that the NPV of investments in each target year is equivalent to the NPV we would obtain in those years when running the 20-year rolling horizon, so the build-out in both models is equivalent too.
2030
2035
2040
2045
2050
2030
2031
2032
2033
2034
= 2030
= 2031-2035
= 2036-2040
= 2041-2045
= 2046-2050
Target Years
Base units
2025-2030
2030-2040
2040-2050
2050-2060
FO&M Charge: OPEX
[€/kW/yr]
Build Cost:
CAPEX
[€/kW]
WACC:
Discount Rate
6%
Economic Life
[yr]
Max Units Built*:
2025-2050
Max Units Built in Year*:
2025-2050
Units built
Each year
Base units
2025-2030
2030-2040
2040-2050
FO&M Charge: OPEX
[€/kW/yr]
Build Cost:
CAPEX
[€/kW]
WACC:
Discount Rate
6%
Economic Life
[yr]
Max Units Built*:
2025-2050
Max Units Built in Year*:
2025-2050
Units built
Each year
= €/kW/5yr
2030-2035
2030-2035
Max Units Built in 5 Years
/5yr
Each 5 years
2030-2031
2031-2032
2032-2033
2033-2034
2034-2035
2035-2036
2022 APPROACH
2024 APPROACH
?%

## Slide 44: LT approach – discount rate adjustment
Problem: In order to obtain a similar build-out as in the 20-yr model, the discount rate of the 5-yr model objective function needs to be adjusted.
In the 20-yr model, the Net Present Value (NPV) calculation follows this expression:
where dfk is the discount factor of year k:
with r = discount rate.
In the 5-yr model, NPV will be:
What should be the discount rate R for the 5 years modelling?

## Slide 45: Discount rate – 1. Discount factors alignment
Hypothesis 1: All investments are done on every target year (every 5 years).
Hypothesis 2: The new discount rate must equalise the discount factor of each target year (2030, 2035, 2040, 2045, 2050).
We have:
(with k = 1 to 5 the years of simulation)
(with r and R the discount rates of the 20 and 5 years simulation respectively)
For a r = 10%, we get R = 61%
The discount factors are equalised to those of the target years
Year | 20 years model | 5 years model
2030 | 1.000 | 1.000
2031 | 0.909 | 0.621
2032 | 0.826 | 0.386
2033 | 0.751 | 0.239
2034 | 0.683 | 0.149
2035 | 0.621 | 
2036 | 0.564 | 
2037 | 0.513 | 
2038 | 0.467 | 
2039 | 0.424 | 
2040 | 0.386 | 
2041 | 0.350 | 
2042 | 0.319 | 
2043 | 0.290 | 
2044 | 0.263 | 
2045 | 0.239 | 
2046 | 0.218 | 
2047 | 0.198 | 
2048 | 0.180 | 
2049 | 0.164 | 
2050 | 0.149 |